## Slide 1
Dr. Asif Zaman
Professor, CSE, RU
ICE 3161
COMMUNICATION ENGINEERING

## Slide 2: Composite Signals
Pure sine wave:
    The sine wave is carrying energy;
    The sine wave is a signal of danger.
…1900s, the French mathematician Jean-Baptiste Fourier showed that:
  Any composite signal is actually a combination of simple sine waves with different frequencies, amplitudes, and phases.

## Slide 3: Composite Signals
It is very difficult to manually decompose this signal into a series of simple sine waves.
However, there are tools, both hardware and software, that can help us do the job.
We are not concerned about how it is done; we are only interested in the result.
If the composite signal is periodic: the decomposed signals are discrete freq.
Else (nonperiodic):
decomposed are sine waves with continuous freq.

## Slide 4
The frequency of the sine wave with frequency f is the same as the frequency of the composite signal; it is called the fundamental frequency, or first harmonic.
The lowest possible frequency
The sine wave with frequency 3f has a frequency of 3 times the fundamental frequency; it is called the third harmonic.
The third sine wave with frequency 9f has a frequency of 9 times the fundamental frequency; it is called the ninth harmonic.

## Slide 5
…the frequency decomposition of the signal is discrete; it has frequencies f, 3f, and 9f.
Because f is an integral number, 3f and 9f are also integral numbers.
There are no frequencies such as 1.2f or 2.6f.
The frequency domain of a periodic composite signal is always made of discrete spikes.

## Slide 6: Composite Signals (Non-Periodic)

## Slide 7: Bandwidth
The range of frequencies contained in a composite signal is its bandwidth.
  The bandwidth is normally a difference between two numbers.
  For example, if a composite signal contains frequencies between 1000 and 5000, its bandwidth is 5000 − 1000, or 4000.

## Slide 8: Bandwidth

## Slide 11: Digital Signals
information can also be represented by a digital signal.
A 1 can be encoded as a positive voltage and a 0 as zero voltage.
A digital signal can have more than two levels

## Slide 12: Digital Signals
In general, if a signal has L levels, each level needs
log2L bits. For this reason, we can send log24 = 2 bits in part

## Slide 13: Bit Rate
The bit rate is the number of bits sent in 1s, expressed in bits per second (bps)
bit rate (instead of frequency)—is used to describe digital signals.

## Slide 14: Bit Rate

## Slide 15: Digital Signal as a Composite Analog Signal
A digital signal is a composite analog signal.
The bandwidth is infinite.
A digital signal, in the time domain, comprises connected vertical and horizontal line segments
A vertical line in the time domain means a frequency of infinity (sudden change in time);
A horizontal line in the time domain means a frequency of zero (no change in time).
Going from a frequency of zero to a frequency of infinity (and vice versa) implies all frequencies in between are part of the domain.

## Slide 16
If the digital signal is periodic, which is rare in data communications, the decomposed signal has a frequency domain representation with an infinite bandwidth and discrete frequencies
If the digital signal is non-periodic, the decomposed signal still has an infinite bandwidth, but the frequencies are continuous.

## Slide 17: Transmission of Digital Signals
The fundamental question is, How can we send a digital signal from point A to point B?
  …a digital signal by using one of two different approaches:
  baseband transmission or
  broadband transmission

## Slide 18: Transmission of Digital Signals
Baseband Transmission
  Baseband transmission means sending a digital signal over a channel without changing the digital signal to an analog signal.

## Slide 19
Baseband transmission requires :
  we have a low-pass channel, a channel with a bandwidth that starts from zero.
  This is the case if we have a dedicated medium with a bandwidth constituting only one channel.
    For example, the entire bandwidth of a cable connecting two computers is one single channel.
    As another example, we may connect several computers to a bus, but not allow more than two stations to communicate at a time.

## Slide 20
Case 1: Low-Pass Channel with Wide Bandwidth
Case 2: Low-Pass Channel with Limited Bandwidth

## Slide 21: Case 1: Low-Pass Channel with Wide Bandwidth
Note that
  f1 is close to zero, and
  f2 is very high

## Slide 22: Case 2: Low-Pass Channel with Limited Bandwidth
A low-pass channel with limited bandwidth, we approximate the digital signal with an analog signal.
The level of approximation depends on the bandwidth available.
Let us assume that we have a digital signal of bit rate N.
…the worst case, a maximum number of changes in the digital signal.
  sequence 01010101 . . . or
  the sequence 10101010. . . .

## Slide 23: Case 2: Low-Pass Channel with Limited Bandwidth
We need an analog signal of frequency f = N/2.
Let,
  1 be the positive peak value and
  0 be the negative peak value.
We send 2 bits in each cycle; the frequency of the analog signal is one-half of the bit rate, or N/2.
Just this one frequency cannot make all patterns; we need more components.

## Slide 24
Data:10,
the frequency of the analog signal is one-half of the bit rate, or

## Slide 25: Case 2: Low-Pass Channel with Limited Bandwidth
Just this one frequency cannot make all patterns; we need more components.
The maximum frequency is N/2.
let us see how a digital signal with a 3-bit pattern can be simulated by using analog signals
100
101
110
111
000
001
010
011

## Slide 31: Better Wave

## Slide 32: Broadband Transmission (Using Modulation)